## Slide 1: ECE 3130 Digital Electronics and Design
Lab 3
Half Adder and 2:1 MUX
Fall 2016

## Slide 2: Tips
Always save your user-made components!
Always use a user-made component when possible
To move component, Alt + drag
To rotate, click R

## Slide 3: Objectives
Learn how adders and multiplexers work
Build and simulate a half adder
    XOR
    AND
Build and simulate a 2-to-1 multiplexer
    Inverter
    NAND

## Slide 4: What are adders?
Digital circuits that perform addition of numbers
Half adder
  Adds two 1-bit binary numbers
Full adder(next lab)
  Adds three 1-bit binary numbers

## Slide 5: Half Adder
Truth table
Implementation
A | B | Sum | Carry_out
0 | 0 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1
XOR Gate
AND Gate

## Slide 6: XOR
A | B | Output
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
Truth table
Schematic – Option 1

## Slide 7: XOR
Schematic – Option 2

## Slide 8: XOR
Symbol

## Slide 9: XOR
Test circuit schematic
Add labels to inputs & output
These labels will help to easily identify signals in simulation waveforms

## Slide 10: Waveform – XOR

## Slide 11: Propagation(XOR) – tpHL
tpHL = 749.8 p

## Slide 12: Propagation(XOR) = tpLH
tpLH = 869.94 p

## Slide 13: Half Adder - Schematic
NAND + Inverter = AND Gate

## Slide 14: Half Adder - Symbol

## Slide 15: Half Adder – Test circuit

## Slide 16: Half Adder - Waveforms

## Slide 17: What is a multiplexer (MUX)?
A device with multiple inputs and one output
Also known as a data selector or controlled switch

## Slide 18: How does it work?
A MUX has n select lines, 2n inputs and 1 output
The select line chooses which input to pass to the output
2-to-1 MUX
Truth table
S | A | B | Z
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 1
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 1
1 | 1 | 0 | 0
1 | 1 | 1 | 1

## Slide 19: 2:1 MUX Gate Implementation

## Slide 20: MUX 2:1 – Schematic

## Slide 21: MUX 2:1 – Symbol

## Slide 22: MUX 2:1 – Test circuit

## Slide 23: MUX 2:1 - Waveform

## Slide 24: Assignment
Build and simulate a half-adder and a 2:1 MUX
Attach all screenshots into one PDF file, including schematic, symbol, test circuit schematic, waveforms.