## Slide 1: ECE 3130 Digital Electronics and Design
Lab 4
Adders and 4:1 MUX
Fall 2016

## Slide 2: Objectives
Build and simulate a full adder & a 4-bit adder
    XOR
    AND = NAND + Inverter
    OR = NOR + Inverter
Build and simulate a 4-to-1 multiplexer
    Three 2-to-1 MUX’s

## Slide 3: What are adders?
Digital circuits that perform addition of numbers
Half adder
  Adds two 1-bit binary numbers
Full adder
  Adds three 1-bit binary numbers
4-bit adder
  Adds two 4-bit binary numbers & one 1-bit carry in

## Slide 4: Full Adder
Truth Table
Implementation
A | B | C | Sum | Carry
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 1
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 1
1 | 1 | 0 | 0 | 1
1 | 1 | 1 | 1 | 1
    OR Gate = NOR + Inverter

## Slide 5: NOR Gate - schematic

## Slide 6: NOR Gate - symbol

## Slide 7: NOR Gate - waveforms

## Slide 8: Full Adder - schematic

## Slide 9: Full Adder – symbol

## Slide 10: Full Adder – test circuit

## Slide 11: Full Adder – waveforms

## Slide 12: 4-bit Adder

## Slide 13: 4-bit Adder - schematic

## Slide 14: 4-bit Adder - symbol

## Slide 15: 4-bit Adder – simulation
Test your 4-bit adder by setting up inputs:
A=1011, B=0111, Carry_in=1
Simulate it and check the results, which should be:
Sum=0011, Carry_out=1
P.S. A=1011 means A0=1, A1=1, A2=0, A3=1

## Slide 16: What is a multiplexer (MUX)?
A device with multiple inputs and one output
Also known as a data selector or controlled switch

## Slide 17: How does it work?
A MUX has n select lines, 2n inputs and 1 output
The select line chooses which input to pass to the output
4-to-1 MUX has 2-bit select line and four 1-bit inputs, and one 1-bit output

## Slide 18: 4-to-1 MUX
Truth table
S1 | S0 | Output (M)
0 | 0 | A
0 | 1 | B
1 | 0 | C
1 | 1 | D

## Slide 19: 4-to-1 MUX - schematic

## Slide 20: 4-to-1 MUX – symbol

## Slide 21: 4-to-1 MUX – test circuit

## Slide 22: 4-to-1 MUX - waveforms

## Slide 23: Assignment
Build and simulate a Full Adder, a 4-bit Adder and a 4:1 MUX.
Attach all screenshots into one PDF file, including schematic, symbol, test circuit schematic, waveforms.