## Slide 1: ECE 3130 – Digital Electronics and Design
Lab 7
Shift Register
Fall 2016

## Slide 2: Introduction
A shift register is a cascade of flip-flops that allows the bit-wise movement of the data contained within it.
Today we will…
  Design a bidirectional(shift right & shift left), parallel-load shift register using DFFs.
  Implement a clear control to reset the register to 0.

## Slide 3: Shift-register
PIPO – Parallel In, Parallel Out
SIPO - Serial In, Parallel Out

## Slide 4: Schematic Design
Buffer
DFF with clear pin

## Slide 5: BUFFER

## Slide 6: Function table for the register
Mode control |  | Register Operation
S1 | S0 | 
0 | 0 | No change
0 | 1 | Shift Right
1 | 0 | Shift Left
1 | 1 | Parallel Load

## Slide 7
In Mode#1:
Input S0=0, S1=0. Other input pins are not used.
The outputs O1-O4 will not change in this mode.
In Mode#2 (SIPO):
Input S0=1, S1=0. “shift_right” pin is used to provide serial 1-bit input data.
Other input pins are not used.
In Mode#3 (SIPO):
Input S0=0, S1=1. “shift_left” pin is used to provide serial 1-bit input data.
Other input pins are not used.
In Mode#4 (PIPO):
Input S0=1, S1=1. I1,I2,I3,I4 are used to provide parallel 4-bit input data.
Other input pins are not used.
The outputs O1-O4 will be loaded to same value as inputs I1-I4.
For all modes(Mode#1-4):
Input “clk” pin is used to provide clock signal to DFFs.
Input “clear” pin is used to reset all DFFs’ outputs to 0.

## Slide 8: Shift Register

## Slide 9: Symbol of Shift Register

## Slide 11: Assignment
Build and test a Shift Register that has 4 different modes.
Attach all screenshots into one PDF file, including schematic, symbol, test circuit schematic, waveforms.