## Slide 1: ECE 3130 – Digital Electronics and Design
Final Project
4-bit ALU controlled by State Machine
Fall 2016

## Slide 2: Overall Diagram
4-bit ALU
DFFs with clear pin
(Switch on/off)
State Machine
(Controller)
Inputs
Outputs
DFFs with clear pin
(Switch on/off)
Control signals
Inputs

## Slide 3: Part 1: 4-bit ALU
4-bit ALU
A0
A1
A2
A3
B0
B1
B2
B3
R0
R1
R2
R3
R4
R5
R6
R7
Carry/Borrow Out
S1
S0
A0-A3 are 4-bit input data A[3:0].
B0-B3 are 4-bit input data B[3:0].
R0-R7 are 8-bit output data R[7:0]. For multiplication, all 8 bits are needed. For addition & subtraction, only the lowest 4 bits (R0-R4) are needed.
Carry/Borrow Out is 1-bit output data which is used for addition/subtraction.
S0-S1 are 2-bit input data that are used to select operations.

## Slide 4: Part 1: 4-bit ALU
S1 | S0 | Functions
0 | 0 | No change
0 | 1 | A plus B
1 | 0 | A minus B
1 | 1 | A x B
Values of select signal S[1:0] & four functions
Select signal S1 and S0 are controlled and given by State Machine based on different states.
PS. “No change” means the previous calculation results of ALU are held and locked. It’s different from being reset to zero.

## Slide 5: Part 2: DFFs at input side
4-bit ALU
A0
B3
R0
R1
R2
R3
R4
R5
R6
R7
Carry/Borrow Out
S1
S0
Eight DFFs are needed at the input side to provide 8 bits input data for ALU(A0-A3, B0-B3).
The value of clear pin is controlled by State Machine. When it’s at high level, DFF is switched on, and thus ALU is able to obtain the input data. When it’s at low level, DFF is switched off, and thus all the inputs of ALU are zero.
clock
clear
Q
D
clock
clear
Q
.
.
.
.
.
.
.
D
B3
A0

## Slide 6: Part 3: DFFs at output side
Nine DFFs are needed at the output side to send out 9 bits output data of ALU(R0-R7, Carry/Borrow Out).
The value of clear pin is controlled by State Machine. When it’s at high level, DFF is switched on, and thus results of ALU are able to be sent out. When it’s at low level, DFF is switched off, and thus results of ALU cannot be sent out.
clock
clear
Q
D
clock
clear
Q
.
.
.
D
4-bit ALU
A0
A1
A2
A3
B0
B1
B2
B3
R0
Carry/Borrow Out
S1
S0
.
.
.
.
.
R0
Carry/Borrow Out

## Slide 7: Part 4: Moore State Machine -- State Diagram
State 0
[S1,S0]=00
Ie=0
Oe=0
State 1
[S1,S0]=00
Ie=1
Oe=0
State 2
[S1,S0]=01
Ie=1
Oe=0
State 3
[S1,S0]=10
Ie=1
Oe=0
State 4
[S1,S0]=11
Ie=1
Oe=0
State 5
[S1,S0]=00
Ie=1
Oe=1
[X1,X0]=00
[X1,X0]=00
[X1,X0]=00,10,11
[X1,X0]=00,01,11
[X1,X0]=00,01,10
[X1,X0]=00
[X1,X0]=01,10,11
[X1,X0]=01
[X1,X0]=10
[X1,X0]=11
[X1,X0]=11
[X1,X0]=10
[X1,X0]=01
[X1,X0]=01,10,11

## Slide 8: Part 4: Moore State Machine
State 0: Initial state. In this state, all DFFs at both sides are switched off. ALU do not have any input data. No operation is selected for ALU. The output of ALU are not sent out.
State 1: Fetching state. In this state, the DFFs at input side are switched on. Input data are sent into ALU and ready to be calculated.
State 2,3,4: Calculating state. In these states, one of the operations of ALU is selected. Results are calculated out by ALU, but not sent out yet.
State 5: Sending out state. In this state, the DFFs at output side are switched on. The calculation results of ALU are sent out.

## Slide 9: Part 4: Moore State Machine -- Symbol
X0-X1 are 2-bit input data, which is used to determine the next state in State Machine.
A,B,C are 3-bit output data, which are used to indicate the number of current state. In this project, they do not need to be connected to anything.
S0-S1 are 2-bit output data, which are used to provide corresponding select signals of ALU.
Ie is 1-bit output data, which is used to control “switch on/off” of eight DFFs at input side. It should be connected to the “clear” pins of DFFs.
Oe is 1-bit output data, which is used to control “switch on/off” of nine DFFs at output side. It should be connected to the “clear” pins of DFFs.
Moore
State Machine
X1
X0
reset
clock
A
B
C
S1
S0
Ie
Oe

## Slide 10: Symbol of the whole project
Final Project
A0
A1
A2
A3
B0
B1
B2
B3
R0
R1
R2
R3
R4
R5
R6
R7
Carry/Borrow Out
X1
X0
reset
clock
A0-A3 and B0-B3 are used to provide data inputs of eight DFFs at input side.
X0-X1 and reset are connected to corresponding inputs of State Machine.
Clock is used to provide clock signals for both State Machine and all DFFs.
R0-R7 and Carry/Borrow Out are connected to corresponding outputs of nine DFFs at output side.

## Slide 11: Test and Simulation
Moore State Machine should be tested separately to ensure all the functions are correct. For example, all the state transitions under different inputs(X1,X0) are correct. All the corresponding outputs in different states are correct.
For the test of whole project, choose five groups of input data A[3:0] and B[3:0].
For each group of input data, set up proper values of X1-X0 and verify all three ALU operations (addition, subtraction, multiplication).

## Slide 12
Two or Three students per group.
Demonstration date: Wednesday, December 7th.
Report due date: By End of Sunday, December 11th.
  Usual expectations : schematic, waveform and analysis
  Plus: Original Tanner Project file in a zip.